## Slide 1
DJI drone workshop
60 MINUTES / LAPTOP ONLY
01
Fly a DJI Mavic 2 PRO in Webots.
Find the red, green and blue objects.
Use the camera to identify each colour.
Notes: The model uses Webots physics and a custom assisted controller. It is not DJI firmware. No competition.

## Slide 2
Our hour together
20 MINUTES FOR YOUR OWN PRACTICE
02
Time | Activity
0–15 min | Introduction, setup and controls
15–35 min | Find and identify three objects
35–55 min | Your own free practice
55–60 min | Share what you tried
Notes: Install Webots and Python beforehand. Preserve the full twenty minutes for participants to explore.

## Slide 3
What you need
BEFORE THE SESSION
03
Webots R2025a installed on your laptop.
Python 3 installed and selected in Webots.
The whole workshop ZIP extracted.
No extra Python packages are needed.
Notes: Setup guide includes links and Python troubleshooting. Official release: https://github.com/cyberbotics/webots/releases/tag/R2025a

## Slide 4
Opening the world
FILE > OPEN WORLD
04
Open the DJI_Outdoor_Workshop folder.
Go to webots, then worlds.
Open dji_outdoor.wbt.
Start Real-time and click inside the 3D scene.
Notes: Keep all assets and controller folders together. Do not run the Python file separately.

## Slide 5
The drone takes off for you
WAIT FOR READY
05
Automatic takeoff
Wait for READY.
Use the small camera view to look down.
Notes: This scene uses the official Cyberbotics DJI Mavic 2 PRO model with grass, trees, a house and a country sky. Source: https://github.com/cyberbotics/webots/tree/R2025a/projects/robots/dji/mavic

## Slide 6
Your flight controls
CLICK THE 3D SCENE FIRST
06
Key | Action
Arrow keys | Forward, backward and sideways
W / S | Move higher / lower
Q / E | Turn left / right
N | Restart from the launch pad
Notes: Directions follow the drone heading. Height request is limited to 2–8 m. N also clears identified objects and triggers takeoff. Release arrows to slow down and hover.

## Slide 7
A short practice flight
SMALL KEY PRESSES HELP
07
Tap Up to move forward.
Release it and let the drone settle.
Try moving sideways with Left or Right.
Try W and S to change your height.
Notes: Allow a couple of seconds to settle. The physical drone accelerates and decelerates. Turning Q/E changes forward direction.

## Slide 8
How to identify an object
LOOK THROUGH THE DOWNWARD CAMERA
08
Fly over a coloured block.
Centre it in the camera and stop moving.
Press R for red, G for green or B for blue.
Check that the Found counter increases.
Notes: Position must be within 1 m of the matching block and the drone must be roughly level. The participant identifies the colour manually. The program validates position, not computer vision.

## Slide 9
Your task is complete at 3/3
RED / GREEN / BLUE
09
RED / R
GREEN / G
BLUE / B
Look for ALL THREE IDENTIFIED and Found 3/3.
Notes: These are actual camera images from the Webots flight test. Each object counts once. There is no ranking or timer.

## Slide 10
Your next 20 minutes are free
35–55 MINUTES
10
Choose what you want to practise.
Try another route or a different height.
Practise turning and stopping over a block.
Press N whenever you want a fresh start.
Notes: These are optional ideas, not extra requirements. Let participants work independently. No competition or compulsory path planning.

## Slide 11
If something does not work
START WITH THESE CHECKS
11
Problem | What to try
Nothing moves | Start Real-time, then click the 3D scene
No camera view | Drone menu: Camera Devices > camera
Colour does not count | Centre the block, stop, press its letter
Drone is lost or tipped | Press N to restart
Notes: For Python errors, use the setup guide and Webots Console. Camera overlays may be disabled in Overlays menu. Slow computers need more wall-clock time.

## Slide 12
What did you notice?
FINAL 5 MINUTES
12
Which camera view helped you find the blocks?
What changed when you flew higher?
What helped you stop over an object?
Notes: Connect observation from above to rover scouting. This is an introductory exercise, not a statement of current URC competition rules.